## Slide 1
Engineered for Corrosion. Built for Performance.
Smart Stainless Solutions for Cost Optimization in Chemical Plants
Application-driven solutions backed by corrosion expertise, real plant references, lifecycle performance and advanced grade portfolio
Actual Site Image – Fertilizer Storage Shed
Stainless Steel Storage Tanks
Flue Gas Desulfurization– Clad Plates

## Slide 2: Jindal Stainless Leader in Specialized Products
5
#1
Stainless steel producer in India
~₹ 429bn
Revenue (Net)*
50+
Exports to countries
#5
Top Global producer Ex - China
~₹ 55bn
EBITDA*
>120 grades
Diversified High End
Product Mix
3mtpa
Stainless steel capacity
0.2x
Net Debt/Equity*
> 21,000
Manpower (incl. contractual)
*Standalone financials ending March 31, 2026

## Slide 3: Ingenuity Meets Manufacturing Excellence The heart of our operations
HISAR
Capacity - 0.8 MTPA
ODISHA
Capacity – 2.2 MTPA
7
Million Tonnes per Annum

## Slide 4
CONTENTS
01
Apart from Conventional Grades
Recent High Performance Grades
Case Study –Process/Storage Equipment's
Hot Rolled Bonded Plate
JSL In Structural Components
Case Study – Roofing's – Fertiliser Plant
02
03
04
05
06
Case Study – Chequered Plates – SA Area
07
Why Choose Jindal Stainless
08

## Slide 5: Chemical Industry Challenges
Process & Structural Challenges
  Unplanned Plant Shutdowns
  Premature Material Failure
  Toxic Leakage & Safety Hazards
  Plant Downtime – Structural Replacements
  Frequent Maintenance, Repainting
  Safety Risks in Elevated/Inaccessible Areas.
Typical Corrosion-Prone Areas
  Acid handling zones
  Walkways, gratings & platforms
  Storage tanks & process vessels
  Coastal / humid operating environments
  Pipe racks & support structures
Corrosion — A Threat to Plant Reliability, Process Continuity & Safety
Why Stainless Steel- Enhanced corrosion resistance with lower lifecycle, maintenance & improved reliability.
Crevice Corrosion
Concrete Spalling – Rebar Corrosion
Atmospheric Corrosion
Uniform Corrosion – Acid Impeller
Notes: Why Material Selection is Important
  Corrosion Resistance
  Mechanical Strength
  Temperature Compatibility
  Lifecycle Cost
  Safety & Reliability
  Maintenance Requirement
SA, Nitric Acid, PA, Acetylne Acid, HFL, etc
Corrosion is not just a material issue — it directly impacts safety, uptime, sustainability, and profitability

## Slide 6: JSL SS Solutions for Process Equipment
Conventional Grades
  Austenitic – 304L, 316L (PREN >18, PREN>23)
  Ferritic – 410s, 430 etc.
Duplex – Ferritic + Austenitic Phase
  Lean Duplex – 2101, 2304 (PREN >26)
  Duplex- 2205 (PREN > 34)
  Super Duplex - S32750, S32760 (PREN > 40)
Super Austenitic Grades
  316F (PREN >25)
  317L, 317LN, 317LMN (PREN > 29)
  904L (PREN > 34)
  6Mo – UNS S31254 (PREN > 43)
  309Si, 310s – High Temperature Application
Advanced Stainless Steel Grades Beyond Conventional 304/316
Duplex vs Conventional SS304L/SS316L
  ~2× higher strength (450–550 MPa) → upto 30% weight saving
  Higher PREN (~35–40) → better chloride resistance
  Superior SCC resistance
  Applications: Storage Tanks, process equipment, structures
Super Austenitic Grades vs Conventional SS304L/316L
  High PREN (~34–43) → strong pitting resistance
  Excellent acid resistance (phosphoric, sulphuric, nitric)
  Better crevice corrosion resistance
  Applications: Acid plants, storage, highly corrosive environments
Duplex microstructure showing darker etched ferritic regions and brighter austenitic regions
Notes: PREN for 317LNM is 33

## Slide 7: Case Study – Lean Duplex – UNS S32101
Application – PTA Storage Silo
Grade – Lean Duplex -2101
Challenge -
  SS304L could not meet high-load strength and thickness requirements for large-capacity storage silos
JSL Solution:
  Supplied 852 MT of LDSS 2101
  Used in lower shell & cone lining for structural strength with thinner shell- Size - 21m (L) × 9.5m (D)
Impact
  Optimized structural performance
  Greater weight savings ~30%
  Enhanced corrosion and mechanical resistance
* Representative Image Only
Strength Optimization for Large-Capacity PTA Silos
Notes: Application: PTA Storage Silos (API 620 Standard)
Client: Indian Oil Corporation Ltd. (IOCL)
Contractor: Technip
Year?

## Slide 8: Case Study – Super Duplex – UNS S32760
Application – Evaporator & Centrifuge Unit, ZLD System
Grade –Super Duplex -UNS S32750 / S32760
Challenge –
  High Nickel-based alloys involved high cost and long lead times, while conventional grades exhibited corrosion under high-temperature effluent conditions
JSL Solution:
  JSL R&D tested materials in real effluent at elevated temperature. Super Duplex outperformed alternatives in corrosion resistance
Impact
  Replaced high value imports with indigenised Super Duplex SS
  Faster project execution
  Lower lifecycle cost as compared with conventional alloys
SS316L SS317L UNS S32205 UNS S32760
Chemical testing in alkaline water sample at 80 ° C
Grade | Initial Weight (gm) | Final Weight (gm) | Corrosion Rate, mpy
316L | 24.60985 | 24.56231 | 6.08
317L | 23.12367 | 23.11942 | 0.5
UNS S32205 | 18.48601 | 18.48489 | 0.16
UNS S32760 | 26.74936 | 26.74911 | 0.03
Application-Driven Grade Selection with JSL

## Slide 9: JSL Advancing India’s Self-Reliance
EQ Grades (EQ309LMo, EQ316L, EQ309LNb, EQ309L, EQ24.13LNb)
  Clad Strips , Weld Overlay Clads
S30815
  High Temperature Performance, Furnace, Kilns
EN 1.4547/UNS S31254 – PREN>42
  Heat Exchanges, Acid/Chloride Services
316F
  High Machinable Grade
EN1.4841/314
  Super Heater Tubes
UNS S32615 - 5% Si Grade
  Sulphuric Acid, Nitric Acid Absorption Tower
304L-NAG
  Nitric Acid Handling
Alloy Steel – 9Cr1Mo
Expanded High-Performance Grade Portfolio
Corrosion rates in absorption tower environment with 99% Sulphuric acid at 105-115 °C |  | 
Alloy | Corrosion Rate | 
 | mm/y | mpy
304 | 0.02 | 0.8
316 | 0.06 | 2.2
5% Si | 0.005 | 0.2
904L | 0.17 | 6.8
20Cb-3 | 0.08 | 3.2
C-276 | 0.32 | 12.6
B-2 | 2.3 | 91
UNS S32615 –Performance for SA Absorption Towers
Notes: Atmanirbhar Bharat Pitch
Alloy 20- (35Ni-20Cr-3.5Cu-2.5Mo)

## Slide 10: JSL - Innovation – Hot Roll Bonded Plates
Hot Rolled Clad Plates - Innovative composite materials consisting of two metallurgically bonded layers.
  A thin layer of Corrosion Protection Alloy
  Base of High Strength Steel – Cost Effective + High Strength
The metallurgical bond is formed in a meticulously controlled hot-rolling process, ensuring superior quality and durability
C276 + IS 2062 E250
Advanced Clad Solutions - Corrosion Resistance with Structural Strength
Notes: Base Layer - ensuring high strength and toughness

## Slide 11: JSL - Innovation – Hot Roll Bonded Plates
Ultrasonic Test | IASTM A578 Level C, S7 (ASTM A265 Quality Level : Class 1)
Visual & Dimensional Inspection, Surface finish, % Edge Condition | Checked dimensions, surface finish, edge condition, flatness, etc.
Mechanical Properties Bend and Hardness Test | As per ASTM A265
Shear Test | As per ASTM A265
Corrosion Test | As per specifications ASTM A262
Testing & Inspection Ensuring Durability & Quality
Backing Steel | Cladding Alloys
A285 gr A, B, C, | 405, 410S, 430
A516 gr 55, 60, 65, 70 | 304, 304L
A204 gr A, B, C, | 309S, 310S
A387 gr 11, 12, 22, | 316, 316L, 317L
A 537 Cl2, A533 gr C, A533 gr B | 321, 347
API 5L X-42/X-46/X-52/X-56/X-60/X-65/X-70 | 625, C-276, 825
Thickness (mm) | Width (mm) | Length (mm)
8.0-20.0 | 1000-1200 | Up to 8000
Engineered Clad Solutions for Process Industries
Notes: Mechanical Properties - UTS, YS, % Elongation
Comments - Any other type of testing as desired by the customer can be carried out based on mutual agreement

## Slide 12: JSL - In Structural Components
Roofing’s
Chequered Plates
Rebars
Angles, Channels
Cable Trays
Ferritic – Used for: Angles, Channels, Beams, Chequered Plates (Walkways)
  409M – Ferritic + Martensitic Structural, good strength + cost-effective corrosion resistance
  410S – Higher strength, great alternate to Standard Steel Rebars
  430 -
  441 - For Mild-Industrial/Sub Coastal
Austenitic – Chequered Plates/Roofing's – (High Corrosion Resistance)
  304 - Industrial/Chemical Environment
  316 – Coastal + Aggressive Chemical Environment
Lean Duplex – Structural Components in aggressive environments
  2101 – High strength, cost-effective duplex alternative
  2304 – High Strength & better performance

## Slide 13: Case Study – Stainless Steel in Roofing's
Challenge :
  Sulphuric acid mist + phosphoric vapours
  Fluorides & chlorides → pitting corrosion
  Hygroscopic fertilizer dust → retains moisture
  Leakage issues affecting storage safety
  High downtime + maintenance burden
  Structural risks due to corrosion
JSL Solution :
  SS 304 Stainless Steel Roofing, 0.5mm
  Excellent resistance to: Acidic fumes, Fertilizer chemicals, Moisture + salt deposits
  No coating → no failure risk
  Reflects solar radiation → lower heat inside plant
  Maintenance- Minimal
  Higher Safety and Reliability
Long-Life Stainless Steel Roofing for Corrosive Fertilizer Units
GI Sheets – Corrosion issues within 18-24 Months
Current Site Images

## Slide 14: Case Study – Stainless Steel Chequered Plates
Challenge :
  Severe corrosion of MS chequered plates in sulphuric acid plant environment
  Acidic fumes and sulphur-bearing deposits accelerated plate deterioration
  Frequent replacement leading to high maintenance and downtime
  Corrosion-induced safety risks in operating walkways and platform areas
JSL Solution :
  SS 409M Stainless Steel chequered Plates
  Improved resistance to sulphuric acid fumes, moisture and chemical deposits
  Cost effective with extended service life
  Reduced Maintenance
  Improved - Safety and Reliability
Corrosion-Resistant Flooring for High-Corrosion Applications
MS Chequered Sheets – Corrosion issues within 18 Months
Actual Site Images –post change to 409M

## Slide 15: Why Choose Jindal Stainless
Backed by R&D grade expertise
BUILT TO LAST
BUILT TO PERFORM
Multiple Grades & Sizes
120+ Grades
Proven in real plants
Built for tough environment
Assurance

## Slide 16
FOR ENQUIRIES / DISCUSSIONS
Meet us at Stall 17
or
Drop an email at mayank.agarwal@jindalstainless.com
salesdevprocess@jindalstainless.com